## Slide 1: A Seymour Cray Perspective
Seymour Cray Lecture Series
University of Minnesota
November 10, 1997
Gordon Bell
Microsoft Corp.
See also: http://www.si.edu/resource/tours/comphist/cray.htm
Notes: <number>
Thank you for inviting me to give this lecture. This is really a great opportunity to think about Seymour Cray and his contributions. I’ve enjoyed just thinking about him in this way.

## Slide 2: A Seymour Cray Perspective
Supercomputing 1999
12 November 1998
Gordon Bell
Microsoft Corp.
See also: http://www.si.edu/resource/tours/comphist/cray.htm http://www.cray.com/hpc/seymour/essay.html
Notes: <number>
Thank you for inviting me to give this lecture. This is really a great opportunity to think about Seymour Cray and his contributions. I’ve enjoyed just thinking about him in this way.

## Slide 3: GB Thought in 1965 on hearing of 6600 – Holy s***!
PDP- 6 was being built
10x less expensive (300K vs. 3 M)
6600 600K transistors; 4 Phase, 10 Mhz clock
“6” had 2 bays x 10-5”crates x 25 = 500 modules
  Clock ran asynchronously at 5 MHz.
  PDP-10 ran at 10 MHz.
<10 transistors/module = 5,000 transistor

## Slide 4: Cray Computer Companies

## Slide 5: Abstract
Cray was the ultimate "tall, thin man"*. I viewed him as being the greatest computer builder that I knew of as demonstrated by his designs and their successors that operated at the highest performance for over 30 years. His influence on computing has been enormous and included: circuitry, packaging, plumbing (the flow of heat and bits), architecture, parallelism, and compilers to exploit parallelism.
*Carver Mead: “one who works at every level of integration from circuits to application software”
Notes: <number>

## Slide 6: Cray 1925 -1996
Notes: <number>
Cray was the penultimate "tall, thin man"*. I viewed him as being the greatest computer builder that I knew of as demonstrated by his designs and their successors that operated at the highest performance for over 30 years… the “Ferrari for supercomputers”. He created the class of computers we know as supercomputers.
His influence on computing has been enormous and included: circuitry, packaging, plumbing (the flow of heat and bits), architecture, parallelism, and programming of the compilers to exploit parallelism… and the problems themselves.
*Carver Mead: “one who works at every level of integration from circuits to application software”

## Slide 7: Circuits and Packaging, Plumbing (bits and atoms) & Parallelism… plus Programming and Problems
Packaging, including heat removal
High level bit plumbing… getting the bits from I/O, into memory through a processor and back to memory and to I/O
Parallelism
Programming: O/S and compiler
Problems being solved
Notes: <number>
Cray worked at every level of integration from the packaging, circuitry, through the operating system, compiler and applications. Part of his success was his ability and willingness to work at all levels and understand every one of them deeply. He excelled at five P’s: packaging, plumbing, parallelism, programming and understanding the problems or apps.
By plumbing I include both the bits and heat flow. A lot of computing is a plumbing problem: deciding on bit pipes, reservoirs or memories, and interchanges (switches). Are there big enough pipes? And are the reservoirs big enough? After all what is a processor other than just a pump. Memory is a storage tank. Gene Amdahl’s rules state that for every instruction per second you need a byte of memory to hold it and one bit per second of I/O. That carries into Cray’s rule for every flops or floating-point operation per second you need a word of memory for holding the results and two memory accesses of bandwidth!

## Slide 8: Seymour Cray Computers
1951: ERA 1103 control circuits
1957: Sperry Rand NTDS; to CDC
1959: Little Character to test transistor ckts
1960: CDC 1604 (3600, 3800) & 160/160A
Notes: <number>
Cray came to the the University of Minnesota under the WW II G.I. Bill, got a BSEE, then a masters the next year in Math. He went to Electronic Research Associates (ERA) and virtually started designing computers and leading and teaching others the day he arrived. He was given the job of designing the control for the ERA1103, a 36-bit scientific computer that Unisys still produces.
He was the chief architect and designer for Univac’s Navy Tactical Data System computer. ERA was bought by Remington-Rand, became part of Univac, and now Unisys. The first merger created the impetus for the ERA founders to form Control Data.
In 1957, when CDC started, Cray put together the “little character”, a six bit computer to test circuits for the first CDC computer, the 160 --- the IO computer for the 1604. So here’s an idea that Cray pioneered: use little computers to do IO for larger computers. The 3600 series followed and held CDC until the 6600 was born in the mid-60s.

## Slide 9: CDC: The Dawning era of Supercomputers
1964: CDC 6600 (6xxx series)
1969: CDC 7600
Notes: <number>
The 6600 influenced architecture probably more than any other computer. It was well plumbed in every respect: it had tremendous bandwidth that interconnected all the components. All computer designers would do well to study it.
CDC built a number of compatible versions, including a dual processor. The 7600 was upward compatible and heavily pipelined. It was to be a prelude to the vector processor.

## Slide 10: Cray Research Computers
1976: Cray 1... (1/M, 1/S, XMP, YMP, C90, T90)
1985: Cray 2 GaAs… and Cray 3, Cray 4
Notes: <number>
The Cray 1 was the first successful vector processor. Others had tried with the Illiac IV, CDC Star; TI ASC, and IBM array processor. The Cray 1 was extended with various models before Steve Chen extended it in the XMP as a shared memory multiprocessor. This became the new basis for improving speed through parallelism with each new generation.
Shared memory vector multiprocessors became the formula for scientific computing that is likely to continue well into the 21st century.
This has been modified to interconnect vector computers, forming a giant multicomputer network to gain even more parallelism at even higher prices. I don’t know whether Cray Research will continue with the vector architecture but certainly Fujitsu, NEC and Hitachi continue to believe it is the future..

## Slide 11: Cray Computer Corp. And SRC Corp. Computers
1993: Cray Computer Cray 3
1998?: SRC Company large scale, shared memory multiprocessor
Notes: <number>
After the Cray 1, he went on to the Cray 2, that was incompatible and not as cost-effective because he tried to simplify the Cray 1 architecture. If Cray 1 was the most expensive love seat; the Cray 2 was the most expensive fishbowl. It was so called because a liquid coolant was pumped among the modules. I saw the largest one with 8 processors at Livermore.
He took the Cray 2 design and the Cray 3 using gallium arsenide to form Cray Computer.
In 1987 SRC was formed to build computers using Intel CMOS Microprocessors.
Just before his death, Peter Cochrane, head of research at British Telecom asked Seymour: “What do you do for a hobby?” Seymour replied: "At home I have a small shop where I build really fast computers..."

## Slide 12: Cray contributions…
Creative and productive during his entire career 1951-1996.
Creator and un-disputed designer of supers from c1960 1604 to Cray 1, 1s, 1m c1977… XMP, YMP, T90, C90, 2, 3
Circuits, packaging, and cooling…
“the mini” as a peripheral computer
Notes: <number>
Let’s look at his amazing 45 year creative and productive career. He was the undisputed designer of Supercomputers… He created the supercomputer class because he didn’t take cost as a constrain. His goal was simple: to build the world’s fastest machine.
Many contributions in the form of circuits, packaging, and cooling.
I was influenced by the 160 to create the minicomputer industry. This was a 12 bit computer when the Von Neumann architecture for scientific computing called for long words. UNIVAC said computers had to be decimal because people didn’’t understand binary.
DEC started out with 18 bit computers, and when an application came up that could have been hard wired logic, I said “a tiny computer is a better alternative”. He saw the 160 as an IO computer.

## Slide 13: Cray Contribution
Use I/O computers
Versus
Use the main processor and interrupt it for I/O
Use I/O channels aka IBM Channels
Notes: <number>
One of his themes was using a computer for IO as opposed to the channel architecture of the 360. My own philosophy is using the main processor for IO and when you run out of capacity, add another processor. This gives you a fungible pool of resources.
Thus, there are three ways of dealing with the outside peripheral world. Do it with the processor and take interrupts; do it with another computer; or use IO channels and programs a la IBM and run special programs that are always interrupting the central processor. I think his view of using IO Computers for the type of machines he built was the right way.

## Slide 14: Cray Contributions
Multi-theaded processor (6600 PPUs)
CDC 6600 functional parallelism leading to RISC… software control
Pipelining in the 7600 leading to...
Use of vector registers: adopted by 10+ companies. Mainstream for technical computing
Established the template for vector supercomputer architecture
SRC Company use of x86 micro in 1986 that could lead to largest, smP?
Notes: <number>
John Cocke, the father of RISC said the 6600 influenced him most. Many of the RISC ideas were in the 6600 or 7600. The basic notion was putting the control complexity in the compiler and building hardware so that all functional units could operate in parallel.
The idea of multi-threading a single processor with independent processor states was used in the ten 6600 Peripheral Processing Units. It ran 10 concurrent 12 bit computers on a time-share basis with 51 bits of state in the processor going through a single hardware interpreter each minor cycle of 100 nanoseconds. The effect was to operate at 5-10 Mips. Bull’s Gamma 60, the Honeywell 800 and Lincoln Laboratory TX-2 used a form of multi-threading of a single processor.
He established vectors as an architecture component.
His influence may continue beyond his death with SRC as it attempts to build the world’s largest flat memory smP using Intel microprocessors.

## Slide 15: Cray attitudes
Didn’t go with paging & segmentation because it slowed computation
In general, would cut loss and move on when an approach didn’t work…
Les Davis is credited with making his designs work and manufacturable
Ignored CMOS and microprocessors until SRC Company design
Went against conventional wisdom… but this may have been a downfall
Notes: <number>
It isn’t clear he was always right. One trend he bucked was to use address translation, including paging because it introduced another memory lookup for every memory access. This made the porting of UNIX to the Cray 1 difficult. The main reason was the small memory for a 64-bit computer.
In general he moved from project to project, often before completing the last. Les Davis is often credited of finishing his designs and making them work. He had no Les Davis at Cray Computer.
He went against conventional wisdom of using VLSI, CMOS by sticking with GaAs without industry’s support. This may have contributed to his lack of success in the 90s with the Cray 3 and 4. All of the technology was unique.

## Slide 16: “Cray” Clock speed (Mhz), no. of processors, peak power (Mflops)
Notes: <number>
Here is the history of Cray machines as measured by floating-point performance, number of processors, and clock speed (or circuitry).
The purple squares show the number of processors per computer.
Blue diamonds show clock speeds in Mhz that were approaching a gigahertz.
The Xs show the aggregate megaflops. In the last ten years all of the performance has come by adding more parallelism to the processors.
I’ve added the last machine that he was working on at SRC Company - it’s in the Teraflops range and its several hundred commodity CMOS microprocessors access a common memory via a large, cross-point memory.

## Slide 17: Time line of Cray designs
control
vector
control
packaging,//
pipelining
circuit
NTDS Mil spec 1957)
Notes: <number>
This is a time line from the Brooks and Blaauw book starting from the ERA 1103. The now Unisys 1100 series is still being built and checking our taxes at the IRS. This branched when CDC was founded. The 1604 and 3600 were compatible. Not shown is the 160 that was a template for the minicomputer. The 6600 line begot the 7600 and later Cyber series computers.
Cray had nothing to do with the STAR, Cyber 205 and ETA 10, all of which were dead end because of their poor scalar performance. Starting Cray Research was a reaction to the STAR and the need for scalar performance in parallel computers. The Cray1 processor design was the template for all high performance computing that will continue well into the 21st century. After the Cray 1, performance was gained by using multiple, vector processors. This architecture was emulated in minisupercomputer designs at Alliant, Ardent, Convex, and many other startups. The Japanese supercomputers at Fujitsu, Hitachi, and NEC use the vector processor architecture formula.

## Slide 18: Univac NTDS for U. S. Navy. Cray’s first computer
Notes: <number>

## Slide 19: NTDS Univac CP 642 c1957
30 bit word AC, 7XR 9.6 usec. add 32Kw core 60 cu. Ft., 2300 #, 2.5 Kw $500,000
Notes: <number>
This is the 1957 NTDS at the Computer Museum History Center at Moffett Field. At 2300 pounds you could actually drop this military computer on your enemies and do a lot of damage. It is very compact and very densely packed with logic.

## Slide 20: NTDS logic drawer 2”x2.5” cards
Notes: <number>
Here’s a logic drawer - one of these pull out drawers holds 5 square inch modules with two or three transistors per card.

## Slide 21: Control Data Corporation Little Character circuit test, CDC 160, CDC 1604
Notes: <number>
Let’s look at Control Data’s first computers. While Cray was not part of the first group who left ERA to found CDC, when he arrived he quickly organized them around the idea of building a high performance computer for scientific calculations.

## Slide 22: Little Character Circuit test for CDC 160/1604 6-bit
Notes: <number>
This is a the Little Character. It had a half dozen rows of logic with about 100 boards per row. The boards are a little bigger than those in the NTDS.
It was built to test new transistor circuitry and clocking.

## Slide 23: CDC 1604
1960. CDC’s first computer for the technical market.
48 bit word; 2 instructions/word … just like von Neumann proposed
32Kw core; 2.2 us access, 6.4 us cycle
1.2 us operation time (clock)
repeat & search instructions…
Used CDC 160A 12-bit computer for I/O
2200# +1100# console + tape etc.
45 amp. 208 v, 3 phase for MG set
Notes: <number>
Note the characteristics of the 1604. It had to compete with the IBM 7090 and Univac scientific computers that had 36-bit words. Those were the days when characters were 6 bits. A long word was significant because it meant accuracy.
Although the machine was somewhat slower than an IBM 7090 with its 2.2 microsecond memory, the longer word length helped by avoiding double precision arithmetic and having two instructions per word.
The architecture had a repeat instruction that in effect, operated like a vector instruction. This speeded operation time up by not requiring the repeating instruction to be fetched. This was useful for searches and data moves.
I copied the idea in the PDP-6 (and later DEC System 10s) into an instruction called BLT for block transfer. This was the antecedent of the bit block transfer or BLIT instructions.
Another significant feature was the use of the external CDC 160 computer for IO.
As you can see it was relatively massive in size and used considerable power

## Slide 24: CDC 1604 module
Notes: <number>
This relatively small module could hold 6-8 transistors. The modules were used for both the 160 IO Computer and the 1604.

## Slide 25: CDC 1604 module bay
Notes: <number>
Modules were stored in 16 rows on these massive fold out doors. Fans blew air through the modules for cooling. The machine consumed about 10 Kilowatts of power.

## Slide 26: CDC 1604 with console
Notes: <number>
Here’s an installation. The main computer weighed one ton and the console 1/2 a ton. The tapes weren’t light either. The console, like all consoles of the day, enabled anyone sitting at it to look at every state bit in the computer. The most unreliable part of the computer was the console typewriter.

## Slide 27: CDC 160 12 bit word
Notes: <number>
The CDC 160 was the IO Computer for the 1604.
CDC never seriously marketed the computer as a minicomputer, but a few were sold at a price of over 100,000. Most importantly was that it influenced others to build small computers. Recall that the first computer designs were for word lengths of 40 bits. IBM and Univac were building 36 -bit computers.

## Slide 28: The CDC 160 influenced DEC PDP-5 (1963), and PDP-8 (1965) 12-bit word minis
Notes: <number>
The 160 influenced the design of the first minicomputers. Like the 160, Digital’s PDP-5 (c1963) was designed for IO. The PDP-8 shown here was introduced in 1965 to be used as with other equipment as a controller or data collection device for real time.
This started the minicomputer industry and making the smallest machine you can to be integrated in other devices for instrumentation and for control. The modules were compatible in size with the IBM SMS modules that were made for high volume production and back panels could be wired by machine. We could manufacture these computers at comparatively low costs. The 160 was priced about $100,000 in 1962, the PDP8 cost $18,000 in 1965. Even the PDP-5 that preceded the 8 cost only $27,000.

## Slide 29: CDC 1604 Classic Accum. Multiplier-Quotient; 6 B (index) register design. I/O transfers were block transferred via I/O assembly registers
Notes: <number>
This is the simplest machine structure you will see outside of an early minicomputer. It was an early classical machine, arithmetic was done in its single accumulator (A) and multiply quotient (Q) registers. That was the way everyone built computers in the beginning because registers were so expensive. There were six index or (B) registers. Data is transferred between the 1604 and IO (either a tape controller or the CDC 160) via 3 Input and 3 Output channels that operate concurrent with the main program. In addition there is a block transfer instruction for the high speed transfer of data. Program interrupt was used to synchronize the various IO transfers.

## Slide 30: Norris & Mullaney et al
Notes: <number>
Bill Norris, the founding President and Frank Mullaney a VP as they were shipping the first machine.

## Slide 31: CDC 3600 successor to 1604
Notes: <number>
The 3600 was an upward compatible successor to the 1604 and quite beautiful. It had smoked glass panels and the logic was behind the glass panels. If you’re going to pay several million dollars for a computer they felt it should look solid and stunning. Another form of packaging. The 3600 carried CDC during the early 60s until the 6600 was available.
Cray worked on the circuitry for the 3600 en route to the 6600.

## Slide 32: CDC 6600 (and 7600)
Notes: <number>
I just can’t tell you how impressed I was when I first saw the 6600 manual. To begin with it was thin and terse - it was just the most elegant computer that I’d seen, given its incredible speed and inherent complexity. I didn’t begin to understand the complexity or how it really could do.
Everyone’s reaction at looking at the performance numbers was uniformly - “oh my god this thing is fast.” How are they doing all of that? Particularly with a ten megahertz clock but they had four phases - so it was more like a 40 megahertz clock at that time. They were doing floating point operations in 3 cycles - floating point is 300 nanoseconds - so how was he doing it so fast because we were sweating to build an order of magnitude slower unit at the time..

## Slide 33: CDC 6600 Installation
Notes: <number>
Let’s look down on the floor of a 6600. It was the big plus sign you see. Sitting next to it is the operator’s console that contained two CRTs.

## Slide 34: CDC 6600 operator’s console
Notes: <number>
The PPUs could look at the program state and bring it to the operator. The state of the control for the machine was not visible to the outside. This broke the idea that you needed an indicator for every flip flop in the machine. Stretch and subsequent large 360s of the 1960s had several very large consoles just to show the state of every flip-flop in the machine.

## Slide 35: CDC 6600 logic gates
Notes: <number>
The three doors of logic swung out from each of the four bays of the “plus” sign. A refrigeration compressor is located in the end of each bay behind the closed door. The goal was to minimize the length of the interconnection wiring by concentrating it all in the intersection of the four bays or twelve doors.

## Slide 36: CDC 6600 cooling in each bay
Notes: <number>
This is the refrigeration compressor that was housed at the ends of each of the four bays. It removed the heat from the cold plates that held the modules. Freon was pumped through the plates to cool them. The heat from each compressor was carried away from the compressor by chilled water. The water of course was chilled by another heat exchanger. Heat from the computer could be used to heat the building.

## Slide 37: CDC 6600 Cordwood module
Notes: <number>
Two 3 by 3 inch printed circuit boards form the outside wiring for what were known as cordwood modules. Transistors and other discrete components were mounted inside in a cordwood fashion to get high density. The packaging figure of merit measure was operations per cubic inch.

## Slide 38: SDS 920 module 4 flip flops, 1 Mhz clock c1963
Notes: <number>
Let’s look at a printed circuit module that was typical of the early 1960s. This one from Scientific Data Systems (that was sold to Xerox Corp. before it was written off) was a lower cost, higher volume machine. SDS was a competitor of DEC and the logic operated at a 1- 2 Mhz clock.

## Slide 39: CDC 6600 modules in rack
Notes: <number>
The cordwood modules were mounted between two plates that were cooled by a refrigeration unit. Note the test points on the modules. No space was taken up for air movement because heat was carried away by conduction.
This gave it a very high packing density enabling short interconnections and high speed.

## Slide 40: CDC 6600 1Kbit core plane
Notes: <number>
This is a 4 Kilobit core memory plane in a 64 x 64 array. Twelve planes were stacked together as a module that had a cycle time of one microsecond and 200 nanosecond access time. The 6600 had many memory modules because you needed 5 for its 60-bit word. Ten for the PPU’s, then 32 banks of 60 bit words meant 32 times five or 4 K 170 modules in the 128 Kiloword machine.
By having 32 banks of one microsecond memory, the bandwidth was in theory 32 Million words per second or roughly 256 Mbytes/second. The machine could operate at roughly 3 Million floating point ops per second. This meant that the processor was unlikely to be waiting because of memory conflicts.

## Slide 41: CDC 1600 & 6600 logic & power densities
Notes: <number>
This graph taken from Jim Thornton’s book on the Design of A Computer, The Control Data 6600 compares the 6600 with the 1604. It made 5 times more logical decision per cubic foot. And the power per logical decision was half. Together this gives a factor of 10. Still the machine was much larger because of the parallelism so there were many more decisions to make.
The impressive thing about the machine was that it used a 10 Mhz clock which is defined to be a minor cycle. The clock had 4 phases, so a lot could be done in a minor cycle especially since combinatorial logic was used extensively.
Floating point adds and multiplies took only 400 and 1000 nanoseconds or 4 and 10 minor cycles respectively. Digital’s PDP 6, a project I headed headed, used a 10 Mhz clock, the add time varied from 400 to 3000 nanoseconds. So I was very impressed with the speed. The 6600 difference was architecture, packaging, and the additional components to increase speed.

## Slide 42: CDC 6600 block diagram
Notes: <number>
The Thornton book is really great because it contains both the design philosophy and the design. It describes their quest for both speed through circuitry and parallelism. It is also a must read for every computer architect.
One principle was that all parts of the computer should operate asynchronously and independently. To begin with all IO devices could independently. Next any IO channel could be assigned to any IO device so that the channel doesn’t become a bottleneck. Finally, any IO Channel could be assigned to any of the ten IO Peripheral Processing Units or PPUs. PPUs were totally independent 12 bit computers similar to the CDC 160. All PPUs could transfer data to the central memory. There was unbound flexibility for the transfer of data into the large computer’s memory. Of course the central memory was accessed by the main processing unit where all the floating point computation was carried out on 60-bit words.

## Slide 43: CDC 6600 registers
Notes: <number>
The processor state consisted of 3 groups of highly functional registers: of the eight 18-bit registers for memory access, 6 control loads, and 2 control stores to the corresponding eight 60-bit floating point registers; and there are eight 18-bit registers for integer and indexing operations. Operations could be carried out simultaneously on multiple registers in each group as long as there was no data interlock.
Data trunks carried information from registers to memory and to the functional units.
Of the functional units, 4 are for carrying out 60-bit floating point arithmetic among the 8 X registers. The other 6 carry out logic, indexing, and program control on the address, A and increment / index, B registers.
The control for managing the parallelism and interlocking was handled in two units called the stunt box and Scoreboard.
Instruction parallelism comes from an 8 word stack.

## Slide 44: Dave Patterson… who coined the word, RISC
“The single person most responsible for supercomputers.
Not swayed by conventional wisdom, Cray single-mindedly determined every aspect of a machine to achieve the goal of building the world's fastest computer.
Cray was a unique personality who built unique computers.”
Notes: <number>

## Slide 45: Blaauw -Brooks 6600 comments
Architecturally, the 6600 is a “dirty” machine -- so it is hard to compile efficient code
Lack of generality. 15 & 30 bit insts
Specialized registers: integer, address, floating-point!
Lack of instruction symmetry.
Incomplete fixed point arithmetic
…
Too few PPUs
Notes: <number>
In their 1997 book, Computer Architecture, Blaauw and Brooks criticize the 6600 as fundamentally being ad hoc. In nearly all of the Cray designs, there is an assumption that it can be programmed to exploit the inherent parallelism of a functional design.
The criticisms such as the specialized registers though valid, fail to acknowledge the implications of a single register set would have on implementation and the difficulty of control with a more general register structure. Because there were 3 different types of registers, allowed for functional parallelism and simpler control and more limited fanin/fanout than with a larger set of registers.

## Slide 46: John Mashey, VP software, MIPS team (first commercial RISC outside of IBM)
“Seymour Cray is the Kelly Johnson of computing. Growing up not far apart (Wisconsin, Upper Michigan), one built the fastest computers, the other built the fastest airplanes, project after project.
Both fought bureaucracy, both led small teams, year after year, in creating awe-inspiration technology progress.
Both will be remembered for many years.”
Notes: <number>

## Slide 47: Thomas Watson,IBM CEO 8/63
“Last week Control Data … announced the 6600 system. I understand that in the laboratory developing the system there are only 34 people including the janitor. Of these, 14 are engineers and 4 are programmers … Contrasting this modest effort with our vast development activities, I fail to understand why we have lost our industry leadership position by letting someone else offer the world’s most powerful computer.”
Notes: <number>
This wonderful quote by Watson encapsulates the issue of the quality and size of a design team together with the right idea to beat any other organization or product.
Also note that one relatively junior engineer had a PhD.

## Slide 48: Cray’s response:
“It seems like Mr. Watson has answered his own question.”
Notes: <number>

## Slide 49: Effect on IBM: market & technical
1965: IBM ASC project established with 200 people in Menlo Park to regain the lead
1969 the ASC Project was cancelled. The team was recalled to NY. 190 stayed.
Stimulated John Cocke’s work on RISC.
Amdahl Corp. resulted (plug compatibles and lower priced mainframes, master slice)
IBM pre-announced Model 90 to stop CDC from getting orders
CDC sued because the 90 was just paper
The Justice Dept. issued a consent decree.
IBM paid CDC 600 Million + ...
Notes: <number>
The 6600 caused IBM to respond in two ways: to examine a new architecture, ASC that was ultimately cancelled; and the pre-announcement of a computer that was yet to be designed and delivered in order to stop CDC from getting orders.
The technical fallout was enormous. Cocke worked on compilers that resulted in the RISC idea as previously stated. Trained engineers helped establish the computer industry in Silicon Valley. Amdahl Corporation was formed to make 360 plug-compatible computers. Custom chip design using the gate array or master slice concept resulted from the Amdahl design. Amdahl formed a partnership with Fujitsu corporation that enabled the Japanese to enter the plug-compatible computing business.
CDC sued and won.

## Slide 50: CDC 6600
Fastest computer 10/64-69 till 7600 intro
Packaging for 400,000 transistors
Memory 128 K 60-bit words; 2 M words ECS
100 ns. (4 phase clock); 1,000 ns. cycle
Functional Parallelism: I/O adapters, I/O channels, Peripheral Processing Units, Load/store units, memory, function units, ECS- Extended Core Storage
10 PPUs and introduced multi-threading
10 Functional units control by scoreboard
8 word instruction stack
No paging/segmentation… base & bounds
Notes: <number>
This summarizes the 6600s contribution. It began to establish the supercomputer class by being larger, faster, and more parallel than any other computer of the day. The 6600 has to be compared with IBM’s System/360 series e.g. model 65, 75 and later 9x models.
By being larger (measured by the number of components) than all of the other computers of the day it pushed the limits of reliability. Cray’s supposed comment: “Parity is for farmers” related to the 6600 that had no parity.
It introduced the concept of a random access memory hierarchy that was under program control.
It’s Multi-Threading was unique because it really operated 10 threads at 10x the rate of a single computer limited by memory as compared to the Bull Gamma 60, Honeywell H800, and Lincoln Laboratory TX-2. The Multi-Threading Architecture is one candidate for future computers to deal with the memory latency problem.
It was the archetype for RISC.

## Slide 51: John Cocke
“All round good computer man…”
“When the 6600 was described to me, I saw it as doing in software what we tried to do in hardware with Stretch.”
Notes: <number>

## Slide 52: CDC 7600
Notes: <number>

## Slide 53: CDC 7600s at Livermore
Notes: <number>
Unlike the earlier computers, the 7600 was C shaped to save floor space. In effect it was about 25 feet long if stretched out. It was organized to avoid needing communication among all the parts at the highest speed.
This was accomplished by extensive pipelining. This was the main contribution of the 7600 to architecture. It was also the key idea and technology to building vector processors.

## Slide 54: Butler Lampson
“I visited Livermore in 1971 and they showed me a 7600. I had just designed a character generator for a high-resolution CRT with 27 ns pixels, which I thought was pretty fast. It was a shock to realize that the 7600 could do a floating-point multiply for every dot that I could display!
In 1975 or 1976, when the Cray 1 was introduced, ... I heard him at Livermore. He said that he had always hated the population count unit, and left it out of the Cray 1. However, a very important customer said that it had to be there, so he put it back. This was the first time I realized that its purpose was cryptanalysis.”
Notes: <number>
Butler Lampson was clearly impressed by the 7600.
The lecture was videotaped and various individuals have copies.

## Slide 55: CDC 7600
“culturally” compatible with 6600
27.5 ns clock period (36 Mhz.)
3360 modules 120 miles of wire
36 Mega(fl)ops PEAK 60-bit words. Achieved via extensive pipelining of
9 Central processor’s functional units
Serial 1 operated 1/69-10/88 at LLNL
65 Kw Small core (less memory than its predecessor. 512 Kw Large core
15 Peripheral Processing Units
$5.1 M
Notes: <number>
Unlike most designers, the second design of a series seemed to be the right one. The 7600 design lasted longer than any other supercomputer design. It had the highest performance of any computer from its introduction in 1969 till the introduction of the Cray 1 in 1976.
It was upward compatible, but had more PPUs.
It had a peak of 30 times faster than the 6600. This was a good trick, because the clock was not quite 4 times faster. The increase in speed was achieved with pipelining in every functional unit.

## Slide 56: CDC 7600 module slice
Notes: <number>
The small dots were transistors. Note the very large number compared to the NTDS. Board layout was fairly critical. 16 slices were packed together as a module. Test points are shown on the right.

## Slide 57: CDC 7600 12 bit core module
Notes: <number>
This core memory gives an idea of the increase in density compared with the 6600 for the Small Core Memory (SCM) of 64K words… or 1/2 the size of the 6600. This is totally counter-intuitive to what we would expect. However, the speed was accomplished by the operation with the LCM. Access time for the SCM was 4 clock cycles and cycle time, 10 clocks.
Thirty-two overlapping memories had an aggregate bandwith of 36 x 32 or 1152 Mwords per second for a computer that operated at 36 Mega-ops.
The Large Core Memory required 64 clock cycles, so transfers between LCM and SCM occurred in packets of 8 words to more closely match the performance of the SCM.

## Slide 58: CDC 7600 block diagram
Notes: <number>
Here’s an overall block diagram of the 7600. Unlike the 6600, PPUs are not multi-threaded. Up to 15 PPUs can be connected and all 15 channels that connect to the central processing unit can operate in parallel. Some of the PPUs can be located in the CPU cabinet and others occupy separate racks.
By the way, disks and the drum were correspondingly small. A disk was only 40 Mbytes, and the drum was 20 Mbytes.

## Slide 59: CDC 7600 registers
Notes: <number>
So it looks almost identical to the 6600, but with an even smaller central memory. It had a 12 word instruction stack, and 9 functional units, not counting branching. Pipelining made the difference. Only the floating point divide was not pipelined, and it took 20 clocks to execute. All the units except multiply could be given operands every clock cycle. Multiply required waiting two clocks.
Long add, floating point add, multiply, and boolean operations took 2, 4, 5, and 2 clocks to execute.

## Slide 60: CDC 8600 Prototype
Notes: <number>
The 8600 proposed in 1968 was targeted to have 4 processors, an 8 nanosecond clock, and built from discrete circuits. As the team tried to solve the problems of heat and speed. CDC was building its STAR under Jim Thornton, fighting IBM in court, investing in business data processing, and new ventures e.g. the U. of IL Plato system. Budgets were tight.
At this point, the CDC bureaucracy took over with budget cutting. This left Cray no choice except to leave and form Cray Research. Norris was supportive and CDC invested $250K.
By leaving, Cray was able to abandon the use of discrete circuits and to use ECL MSI Circuits that were key to its density and success.
It would be interesting to know whether the 8600 architecture resembled the Cray 1 architecture.

## Slide 61: Forming Cray Research
The STAR 100 >> Cyber 205 >> ETA 10 was the “new mainline” in response to DOE & NASA RFQs
Other investments: IBM anti-trust suit, Business data-processing, and new ventures e.g. U of IL Plato
The 8600 packaging hit a “dead end” and unable to attain its speed
Emergence of MSI ECL. A catalyst?
Unclear how the notion of “vectors” came into the decision
Easy decision to leave… given CDC bureaucracy
Notes: <number>

## Slide 62: Cray Research… Cray 1
Started in 1972, Cray 1 operated in 1974
12 ns. Three ECL I/C types: 2 gates, 16 and 1K bit memories
144 ICs on each side of a board; approximately 300K gates/computer
8 Scalar, 8 Address, 8 Vector (64 w), 64 scalar Temps, 64 address B temps 12 function units
1 Mword memory; 4 clock cycle
Scalar speed: 2x 7600 Vector speed: 80 Mflops
Notes: <number>
In early 1972, Cray and six other colleagues left CDC to form Cray Research. Les Davis was a co-founding chief engineer and is often credited with Cray’s success. Their relationship was characterized by one engineer: “When Seymour tosses designs out the window, Les catches them”.
It was time to use Integrated Circuits.

## Slide 63: Cray 1 scalar vs vector performance in clock ticks
Notes: <number>
This graph of performance in clock ticks for scalar and vector code for vector of various lengths illustrates the advantages of vector processing. Vector operations operated at 7x scalar for the various functions.

## Slide 64: CDC 7600 & Cray 1 at Livermore
Cray 1
CDC 7600
Disks
Notes: <number>
In the background to the Cray 1 is the 7600 that stayed in operation at Livermore till 1988.

## Slide 65: Cray 1 #6 from LLNL. Located at The Computer Museum History Center, Moffett Field
Notes: <number>
An early Cray 1A from Lawrence Livermore National Laboratory at the Computer Museum History Center, located at Moffett Field in Mountain View California. Note the panels on the bottom that house power supplies. The C shape was used to minimize wiring distance in the inner circumference backpanel.

## Slide 66: Cray 1 150 Kw. MG set & heat exchanger
Notes: <number>
The Cray 1 had two of these motor-generators to generate the 3 phase 400 cycle power that was fed to the power supplies located around the base of the computer. Seymour claimed it was the world’s most expensive “love seat”.
The other unit was a large refrigeration unit that pumped Freon into the computer cold plates. Heat was transferred to chilled water that could be used to heat the building.

## Slide 67: Cray 1 processor block diagram… see 6600
Notes: <number>
Operations are carried out in the eight S scalar registers and 8 64-word Vector registers. Vector length is specified in a register and a mask determines which operands participate in a vector operation. Address arithmetic is carried out in the 8 A registers.
Two sets of 64 temporary registers store scalars and addresses to minimize access time.
Instructions are buffered in 4 groups of 64 x16 bits.
It is remarkably similar to the 6600… and extended for vectors.
In addition to operations that operate on fixed strides, a scatter-gather mode is used such that each operand is pointed to by an address.
This basic vector architecture has been implemented in numerous other architectures, including Japan and minisupercomputers. About a dozen manufacturers have copied the “Cray-style’ vector architecture.

## Slide 68: Steve Wallach, founder Convex
“I began working on vector architecture in 1972 for military computers including APL.
“I fell in love with the Cray 1.
  Continue to value Cray’s Livermore talk
  Raised the awareness and need for bandwidth
  Kuck & Kennedy work on parallelization and vectorization was critical
1984: Convex was founded to build the C-1 mini-supercomputer. Convex followed the Cray formula including mPs and GaAs
Notes: <number>
One of the successful computer designers, Steve Wallach, comments on Cray.

## Slide 69: George Spix comments on Cray 1
“But these machines were a delight to code by hand with significant performance rewards for tight and well scheduled assembly. His use of address (A) registers to trigger reading and writing of computational (X) registers brought us optimally scheduled loads and stores driven by a space and time efficient increment, demonstrating again Seymour's intuitive if not intimate understanding of applications' data flow in a minimalist partitioning of function in logic that was, in a word, beautiful.”

## Slide 70: Cray XMP/4 Proc. c1984
Notes: <number>
In 1982 almost a decade after the Cray 1, Cray Research introduced the 2 processor XMP. It was extended to 4 processors in 1984.

## Slide 71: Cray, Cray 2 Proto, & Rollwagen
Notes: <number>
Here’s Cray with John Rollwagen the CEO of Cray Research. In the foreground is a tank that held fluorinert, the liquid that is used for heart transplant. This liquid was pumped directly through the Cray 2 and the heat of the modules boiled the liquid which was then recooled by the refrigeration.

## Slide 72: Cray 2
Notes: <number>
The actual Cray 2 with 8 processors. In the background is the storage unit that held the chilled fluorinert before being pumped into the computer.

## Slide 73: Cray Computer Corporation Cray 3 and Cray 4 GaAs based computers
Notes: <number>
Cray Research could no longer fund the concurrent development of extending the Cray 1 architecture beyond the XMP, YMP, C90, and T90 line.
In 1989 Cray left to form Cray Computer Corporation to finish the development of the Cray 3 GaAs computer that was packaged using gold wire bonding that was robot assembled.

## Slide 74: Cray 3 c1995 processor 500 MHz 32 modules 1K GaAs ic’s/module 8 proc.
Notes: <number>
This was the a processor built from GaAs that was the last operational computer that Cray Computer Corporation built. One two processor(?) computer was delivered to NSA. A second, 4 processor computer operated in 1993 at the National Center for Atmospheric Research before the company folded. Its clock operated at 500 Mhz. Like all the rest, it was the ultimate in density and packaging. It was to have 16 processors.

## Slide 75: Petaflops by 2010
“
”
1994 DOE Accelerated Strategic Computing Initiative (ASCI)
Notes: <number>
In 1997 a massively parallel system with 9,000 microprocessors operated at Sandia Corporation at over 1 Teraflops. Two other computers were being delivered to LLNL and LASL by IBM and SGI/Cray respectively that would also operate at teraflops rates.
This caused the Department of Energy to initiate ASCI aimed at a Petaflops, mimicking DARPA’s 1982 SCI.

## Slide 76: February 1994 Petaflops Workshop
3 Alternatives for 2014
  Each have to deliver 400 Tflops
  Shared memory, cross-bar connects 400, 1Tflops processors!
  Distributed, 4,000 to 40,000 computers @ 10 to 100 Gflops
  PIM 400,000 computers @ 1 Gflops
No attention to disks, networking
Notes: <number>

## Slide 77: Petaflops Alternatives c2007-14 from 1994 DOE Workshop

## Slide 78: Cray spoke at Jan. 1994 Petaflops Workshop
Cray 4 projected at $80K/Gflops, $20K in 1998 sans memory (Mp) .67 cost decr/yr; 41% flops incr/yr
1 Tflops = $20M processor + $30M Mp 1 Gflops requires 1 Gwords/sec of BW
SIMD $12M = 2M x $6/1-bit processors … in 1998 this is 32M for 1 Tflops at $50M
Projected a petaflops in 20 years… not 10!
Described protein and nanocomputers
Notes: <number>

## Slide 79: SRC Company Computer Cray’s Last Computer c1996-98
Uniform memory access across a large processor count. NO memory hierarchy!
Full coherency across all processors.
Hardware allows for large crossbar SMPs with large processor counts.
Programming model is simple and consistent with today’s existing SMPs.
Commodity processors soon to be available allow for a high degree of parallelism on chip.
Heavily banked, traditional Seymour Cray memory design architecture.
Notes: <number>
Perhaps Seymour Cray will produce a posthumous contribution by demonstrating how to put 1000s of commodity microprocessors together to form a flat shared memory multiprocessor. Certainly the design goal is the right one.

## Slide 80: Joel Birnbaum, CTO HP
It seems impossible to exaggerate the effect he had on the industry; many of the things that high performance computers now do routinely were at the furthest edge of credibility when Seymour envisioned them.
I have had the opportunity to work with several of his very talented proteges who went on to other companies, and his considerable legacy as a teacher and mentor has also had a far-reaching effect.
Seymour combined modesty, dedication, and brilliance with vision and an entrepreneurial spirit in a way that places him high in the pantheon of great inventors in any field. He ranks up there with Edison and Bell of creating an industry
Notes: <number>

## Slide 81: Howard Sachs recollection working in Colorado Springs 1979 - 1982
“He was one of the highlights of our industry and I was very lucky to know and work with him.
I learned a tremendous amount from him and was very appreciative of the opportunity. We spent most of the time talking about architectures and software. A significant amount of time was spent discussing the depth of pipelining and vector register startup times.
His style as the project manager was to ask different people to design sections of the machine. They had little direction and were allowed to have a lot of freedom, ...
Notes: <number>
These are my updated notes and still not organized in any particular fashion, just ramblings of my recollections with Seymour. He was one of the highlights of our industry and I was very lucky to know and work with him.
I went to Cray in 1979 and was Vice President in charge of the hardware development for Cray Labs in Boulder Colorado. The lab was closed in the summer of 1982. At that time Seymour was in control of Cray Research as CEO I think, and John Rollwagen was President. Stuart Patterson was president of Cray Laboratories reporting to the Board of Directors of Cray Research, and I reported to Stuart in charge of hardware development. After about a year there was a falling out between Rollwagen and both Seymour and my boss Stuart Patterson. The issue was largely over budgets and as a result Seymour resigned from Cray Research and formed Cray Computer. One of the more important issues was that Cray Research had first right of refusal on all computers that Seymour designed.
My first experience with Seymour was my initial interview. We had a great conversation regarding mostly packaging technologies and cooling. We got into a fairly heated argument of some issue, I just don't remember, but I was impressed with the fact that he seemed to enjoy the argument. After that we had many good spirited discussions.
He worked most of the time at his home and came in to the office about10:00 AM and left at lunch. I met with him monthly at the Haley (sp.) Labs at about 10:00 AM and then we went to lunch and I went back to Boulder and he went home. This was my view, check with others to see if this was his normal habit. This was set up so I could ask questions and learn from him. I learned a tremendous amount from him and was very appreciative of the opportunity. We spent most of the time talking about architectures and software. A significant amount of time was spent discussing the depth of pipelining and vector register startup times.
His style as the project manager was to ask different people to design sections of the machine. They had little direction and were allowed to have a lot of freedom, when they were done they submitted their logic equations to Seymour and he usually never spoke to them about it again. You never knew if he used your logic until the machine was complete. His top logician was Harry Runkle, unfortunately deceased for many years. Harry had a hard time with the lack of feedback, but was a very good guy and put up with it.

## Slide 82: Sachs comments
the team couldn't solve the packaging problems to his satisfaction. As a result he told me to fire everyone, and he said he was through with the Cray 2 and was going to work on operating system issues.
After 6 months or so Seymour called me, he was very excited, because he had solved the Cray 2 packaging problem and wanted me to see it. We were all very surprised, because we thought he was working on operating systems. The approach was the little pogo pins and vapor phase reflow soldering that ultimately went into production. It was quite novel but did not seem to be manufacturable.
Notes: <number>
This is an interesting story about the first Cray 2 machine. I was called to Haley by Seymour to have a Cray 2 review. There was only four or five of us in the conference room and Seymour told us that he was very unhappy with the progress of the machine. Primarily the team couldn't solve the packaging problems to his satisfaction. As a result he told me to fire everyone, and he said he was through with the Cray 2 and was going to work on operating system issues. He also said I should build the new Cray 2. We were all stunned, I remember talking to Les Davis about what to do, Les was head of manufacturing and reported to John Rollwagen, and as a result we didn't fire anyone we just moved a few people around and continued the project in boulder.
After 6 months or so Seymour called me, he was very excited, because he had solved the Cray 2 packaging problem and wanted me to see it. We were all very surprised, because we thought he was working on operating systems. The approach was the little pogo pins and vapor phase reflow soldering that ultimately went into production. It was quite novel but did not seem to be manufactureable. Les Davis was responsible for manufacturing and fought the idea but I guess he got it working somehow. You must talk to Les and get his perspective.
Seymour wanted me to work with Rockwell on a Gas machine at the same time we were working on the Cray 2. I spent a lot of time with the Rockwell people and the design of over 200 individual chips. Keep in mind that at that time there were not many circuit designers in Cray or most computer companies. We had one Calma machine for layout and no circuit designers at the time. I tried to convince Rockwell to make a gate array so the circuit problems wouldn't kill us. They refused, so I killed the program. Seymour and I had a major disagreement over this and he took over the project himself. After many false starts this became the Cray 3 many years later.
One of Seymour's characteristics was that he only returned phone calls from people he knew or knew of, so for many people he was unreachable, but within the company he was very easy to talk to and generally was very pleasant, but certainly not talkative, somewhat quiet.

## Slide 83: Sachs on Logic
Most of us logicians and architects in Boulder all studied the logic for the Cray 1 and found his work to be simple but not obvious. It took a lot of effort to understand some of the features of his logic. Some designs still stick in my mind, his adders were very fast and different, although now the techniques are in all the textbooks and very common. The way he swapped context was quite interesting; the register files were all dual ported so that all the registers could be moving at the same time.
Seymour was a great architect, logician, and packaging engineer but did not understand circuit design or semiconductor technology. During the 60's and70's most of the architects had strong logic design backgrounds. I recall that most of the architects of that time were weak in circuit design and since VLSI was not mature, the architects of the day were generally not experienced with these new capabilities.
Notes: <number>
As a person he was extremely organized, everything was in it's place on his desk at work or in the office in his home. It was interesting that, although he was extremely well organized I don't recall any schedules for projects. He personally took care of training ladies to adjust the length of traces on the printed circuit boards to be the same length, thereby avoiding races. Ladies that had little or no experience did this.
Seymour got married (I think in 1980). My wife (Gail) and I went to dinner one evening with Seymour and his fiancée at the time, and found her to be very charming and outgoing. I recall Seymour got a very expensive bottle of red wine, Chateau Lafite Rothchild approx. $100 per bottle. So I think he must have been interested in wine, perhaps because Rothchild was an investor in Cray and he usually got a case each year as a gift from Rothchild.
Most of us logicians and architects in Boulder all studied the logic for the Cray 1 and found his work to be simple but not obvious. It took a lot of effort to understand some of the features of his logic. Some designs still stick in my mind, his adders were very fast and different, although now the techniques are in all the textbooks and very common. The way he swapped context was quite interesting; the register files were all dual ported so that all the registers could be moving at the same time.
Seymour was a great architect, logician, and packaging engineer but did not understand circuit design or semiconductor technology. During the 60's and70's most of the architects had strong logic design backgrounds. I recall that most of the architects of that time were weak in circuit design and since VLSI was not mature, the architects of the day were generally not experienced with these new capabilities.

## Slide 84: Sachs
We did discuss LSI with Seymour, bipolar of course; CMOS was much too slow and not interesting till 1984 when1 micron CMOS became available. Seymour did encourage me to build a bipolar semiconductor pilot line to build chips for prototype computers. ... I subsequently went to work for Tom at the Fairchild Research Center where I worked on microprocessor development.
There were many discussions about the selling price of the Cray computers, Seymour and John Rollwagen did not want to drop down to 1 million-dollar computers, they wanted to stay at the 10 million range which ultimately destroyed the company (my opinion only). Their customers, the big labs wanted less expensive smaller machines and wanted to experiment with parallel processing at the time.
Notes: <number>
We did discuss LSI with Seymour, bipolar of course; CMOS was much too slow and not interesting till 1984 when1micron CMOS became available. Seymour did encourage me to build a bipolar semiconductor pilot line to build chips for prototype computers. We experimented with 256 gates per chip and used the Fairchild bipolar process. We developed a direct write e-beam front-end process that was used in Boulder in addition to making it available to Fairchild Semiconductor as part of the "quid pro quo" for Fairchild giving us the front end bipolar process. I recall working very closely with Doug Peltzer; he was in charge of bipolar process development during those days as well as Tom Longo. Tom was in charge of Fairchild's research center and was also on the board of Cray Research. I subsequently went to work for Tom at the Fairchild Research Center where I worked on microprocessor development.
There were many discussions about the selling price of the Cray computers, Seymour and John Rollwagen did not want to drop down to 1 million-dollar computers, they wanted to stay at the 10 million range which ultimately destroyed the company (my opinion only). Their customers, the big labs wanted less expensive smaller machines and wanted to experiment with parallel processing at the time.
I understand he was an avid sailboard sailor and built his own boards. I don't recall that he had any other hobbies.
Regards Howard Sachs

## Slide 85: Jim Gray
Seymour built simple machines - he knew that if each step was simple it would be fast.
When asked what kind of CAD tools he used for the CRAY1 he said that he liked #3 pencils with quadrille pads. He recommended using the back sides of the pages so that the lines were not so dominant.
When he was told that Apple had just bought a Cray to help design the next Mac, Seymour commented that he had just bought a Mac to design the next Cray.
Notes: <number>

## Slide 86: Norman Taylor, Lincoln Labs
While at Control Data, I worked with Seymour on a few projects, after which I wrote the following letter to another genius I knew --Glen Culler at UC Santa Barbara.
In my many years in computing, I have met dozens of experts-------von Neumann , Forrester , Everett, Weiner, Wes Clark, all the great people on Project MAC and on and on.
Only two had the breadth to cover all the bases ---Cray and Culler--they crossed the line from math to logical design, to software, to compilers, assemblers, to circuitry, to implementation as if there were no lines to cross.
My favorite Seymour story stems from one close relationship where I was presenting to him a Lincoln idea to improve memory bandwidth--it included building a 600 bit memory to feed his 1060 bit memories on his 6600 model. This was in 1965 or so ---he said in the middle of a sentence, “let’s try it out.”
I will need to make a small hardware change. He grabbed a soldering iron changed a couple of wires--no drawings all from memory. Then said:“I will have to make a little software change.” Three minutes at a keyboard. Then he said, “It's going to work!”
One week later the plant was in production making 600 bit screen door memories of cores.
No committees, a few drawings--and of course new input software.
Norm Taylor via his son, Bob Taylor, Tandem

## Slide 87: The End
Notes: <number>

## Slide 88: References
Notes: <number>

## Slide 89: Supercomputing Next Steps
Notes: <number>
It is important to look at some of the future directions for supercomputing .

## Slide 90: Battle for speed through parallelism and massive parallelism
Notes: <number>

## Slide 91: Parallel processing computer architectures will be in use by 1975.
“
”
Navy Delphi Panel 1969
Notes: <number>

## Slide 92: In Dec. 1995 computers with 1,000 processors will do most of the scientific processing.
“
”
Danny Hillis 1990 bet with Gordon Bell (1 paper or 1 company)
Notes: <number>

## Slide 93: In Dec. 1995 computers with 1,000 processors will do most of the scientific processing.
“
”
Danny Hillis 1990 (1 paper or 1 company)

## Slide 94: The Bell-Hillis Bet Massive Parallelism in 1995
TMC
World-wide
Supers
TMC
World-wide
Supers
TMC
World-wide
Supers
Applications
Revenue
Petaflops / mo.

## Slide 95: Bell Prize Peak Gflops vs time

## Slide 96: Bell Prize: 1000x 1987-1998
1987 Ncube 1,000 computers: showed with more memory, apps scaled
1987 Cray XMP 4 proc. @200 Mflops/proc
1996 Intel 9,000 proc. @200 Mflops/proc 1998 600 RAP Gflops Bell prize
Parallelism gains
  10x in parallelism over Ncube
  2000x in parallelism over XMP
Spend 2- 4x more
Cost effect.: 5x; ECL  CMOS; Sram  Dram
Moore’s Law =100x
Clock: 2-10x; CMOS-ECL speed cross-over
Notes: <number>

## Slide 97: No more 1000X/decade. We are now (hopefully) only limited by Moore’s Law and not limited by memory access.
1 GF to 10 GF took 2 years
10 GF to 100 GF took 3 years
100 GF to 1 TF took >5 years
1 TF to 3 TF took 1 year
2n+1 or 2^(n-1)+1?

## Slide 98: DOE’s 1997 “PathForward” Accelerated Strategic Computing Initiative (ASCI)
1997 1-2 Tflops: $100M
1999-2001 10-30 Tflops $200M??
2004 100 Tflops
2010 Petaflops

## Slide 99
“
”
When is a Petaflops possible? What price?
Moore’s Law 100x But how fast can the clock tick?
Increase parallelism 10K>100K 10x
Spend more ($100M  $500M) 5x
Centralize center or fast network 3x
Commoditization (competition) 3x
Gordon Bell, ACM 1997

## Slide 100: Or more parallelism… and use installed machines
10,000 nodes in 1998 or 10x Increase
Assume 100K nodes
10 Gflops/10GBy/100GB nodes or low end c2010 PCs
Communication is first problem… use the network
Programming is still the major barrier
Will any problems fit it

## Slide 101: End 2

## Slide 102: What Is The Processor Architecture?
VECTORS
VECTORS
OR
CS View
MISC >> CISC
Language directed
RISC
Super-scalar &
Extra-Long Instruction Word
SC View
RISC
VCISC (vectors)
Massively parallel (SIMD)
Notes: <number>
44:20 15

## Slide 103: Is vector processor dead? Ratio of Vector processor to Microprocessor speed vs time
1993 Cray Y-MP IBM RS6000/550 9.4
1997 NEC SX-4 SGI R10k 9.02
2000* Fujitsu VPP Intel Merced 9.00
Notes: <number>

## Slide 104: Is Vector Processor dead in 1997 for climate modeling?
Notes: <number>

## Slide 105: Cray computers vs time
Notes: <number>

## Slide 106: CDC 6600 Console
Courtesy of Burton Smith, Microsoft

## Slide 107: Two CDC 7600s
Courtesy of Burton Smith, Microsoft

## Slide 108: Vector Pipelining: Cray-1
Unlike the CDC Star-100, there was no development contract for the Cray-1
  Mr. Cray disliked government’s looking over his shoulder
Instead, Cray gave Los Alamos a one-year free trial
Almost no software was provided by Cray Research
  Los Alamos developed or adapted existing software
After the year was up, Los Alamos leased the system
  The lease was financed by a New Mexico petroleum person
The Cray-1 definitely did not suffer from Amdahl’s law
  Its scalar performance was twice that of the 7600
  Once vector software matured, 2x became 8x or more
When people say “supercomputer”, they think Cray-1
Courtesy of Burton Smith, Microsoft

## Slide 109: Cray-1
Courtesy of Burton Smith, Microsoft

## Slide 110: Shared Memory: Cray Vector Systems
Cray Research, by Seymour Cray
  Cray-1 (1976): 1 processor
  Cray-2 (1985): up to 4 processors*
Cray Research, not by Seymour Cray
  Cray X-MP (1982): up to 4 procs
  Cray Y-MP (1988): up to 8 procs
  Cray C90: (1991?): up to 16 procs
  Cray T90: (1994): up to 32 procs
  Cray X1: (2003): up to 8192 procs
Cray Computer, by Seymour Cray
  Cray-3 (1993): up to 16 procs
  Cray-4 (unfinished): up to 64 procs
All are UMA systems except the X1, which is NUMA
  *One 8-processor Cray-2 was built
Cray-2
Courtesy of Burton Smith, Microsoft